Welcome to the Cold Saw Replication Guide.

Refer to the document called Build Preparation.

Source material components 101 to 122.

Source tool components 150 to

Prepare following skills:

Use – Combination Square
Use – Speed Square
Use – Measuring Tape
Use – Scribe
Use – Consumable Marking Utensils
Use – Oxyacetylene Torch
Use – Welder
Use – Mill

# Cut Materials
## 2” x 3” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
4 – 26mm (1.0236”) for Short Spacers [Positive Tolerance Only!]
1 – 50.8mm (2”) for Handle Block
4 – 76.2mm (3”) for Long Spacers
4 – 101.6mm (4”) for Clamp Blocks
4 – 127mm (5”) for Clamp Jaws
2 – 300mm (11.81”) for Swivel Blocks
3 – 400m (15.75”) for Vise Moving Blocks and Vise Fixed Block

## 1” x 4” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 140mm (5.513”) for Short Support Flat
1 – 200mm (7.87”) for Bridge Flat
2 – 280mm (11”) for Long Support Flat and Rotation Support Flat

## 1/8” x 1” Steel Flat Lengths
Cut Length Tolerance – 13mm (1/2”)
Cut Angle Tolerance – <5 degree
1 – 101.6mm (4”) for Indicator Flat
2 – 381mm (15”) for Blade Guard Supports
## 3” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
3 – 25.4mm (1”) for Axial-Radial Shaft Collars

## 2” Outer Dia 1.25” Inner Dia Steel DOM Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
6 – 20mm (0.787”) for Shaft Collars
1 – 76.2mm (3”) for Shaft Coupling

## 1.25” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 25.4 (1”) for StopShaft
1 – 90mm (3.54”) for Spindle
4 – 350mm (13.78”) for Vise Shafts, Vise Handle, Support Shaft
## 1.25” Dia 1/8” Thk Round Tube Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 127mm (5”) for Operation Handle Support
1 – 609.6mm (24”) for Operation Handle
# Make Operation Handle
## Mark Bend Length
## Clamp Metal Tube
## Torch Bend Region
## Bend Metal Tube

# Make Raisers
## Mark Metal Flat
Get the 1” x 4” x 11” steel flat.
Mark the flat for 2 raisers as shown below:

## Angle-cut the Metal Flat
Use a speed square to orient the metal flat at 45 degrees on the ironworker.
Remove the speed square.
Clamp the metal flat.
Shear the metal flat!

Reclamp one metal flat for the right cut angles.
Shear the first!
Reclamp and shear the second!

## Surface Grind Top and Bottom
15/1000” for top
2/1000” for bottom

# Make Blade Guard
## Prepare the 1/8” x 1” Steel Flat
2 – 381mm
## Mark
Mark each component.

## Drill Thin Metal Flat
## Bend Thin Metal Flat
## Mount Metal Sheet
## Torch Inner Circle
## Torch Outer Circle
## Torch In Half
## Mount Halves
## Weld Thin Metal Flat
# Short Support Flat
## Mark Hole

## Drill Hole
# Rotation Support Flat
## Mark Holes

Mark a torch-start hole at the circumference of the large hole to be torched.
## Drill Small Holes
## Torch Large Hole
# Long Support Flat
## Mark Holes

## Drill Small Holes
## Drill Large Hole
# Clamp Block
## Mark Holes and Lip

## Drill Small Hole
## Mill Lip
# Clamp Jaw
## Mark Slot
## Mill Slot
# Fixed Block
## Mark Holes
## Drill Small Holes

## Drill Large Holes
# Moving Block
## Mark Hole
Just the center hole.
## Drill Hole
## Align with Fixed Block
Use a shaft through the holes of both blocks.
## Drill-Start Large Holes
## Drill Large Holes