Welcome to the Cold Saw Replication Guide.

Refer to the document named Build Preparation for what tools and materials you will need for making the Cold Saw.

During the Build Preparation, identify and organize the items for ease of access during the replication process.

# Cut Materials
## 2” x 3” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
4 – 26mm (1.0236”) for Short Spacers
1 – 50.8mm (2”) for Handle Block
4 – 76.2mm (3”) for Long Spacers
4 – 101.6mm (4”) for Clamp Blocks
4 – 127mm (5”) for Clamp Jaws
2 – 300mm (11.81”) for Swivel Blocks
2 – 400m (15.75”) for Vise Moving Blocks and Vise Fixed Block

## 1” x 4” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 140mm (5.513”) for Short Support Flat
1 – 200mm (7.87”) for Bridge Flat
2 – 280mm (11”) for Long Support Flat and Rotation Support Flat

## 1/8” x 1” Steel Flat Lengths
Cut Length Tolerance – 13mm (1/2”)
Cut Angle Tolerance – <5 degree
1 – 101.6mm (4”) for Indicator Flat
2 – 381mm (15”) for Blade Guard Supports
## 3” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
3 – 25.4mm (1”) for Axial-Radial Shaft Collars

## 2” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
6 – 20mm (0.787”) for Shaft Collars
1 – 76.2mm (3”) for Shaft Coupling

## 1.25” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 25.4 (1”) for StopShaft
1 – 90mm (3.54”) for Spindle
4 – 350mm (13.78”) for Vise Shafts, Vise Handle, Support Shaft
## 1.25” Dia 1/8” Thk Round Tube Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 127mm (5”) for Operation Handle Support
1 – 609.6mm (24”) for Operation Handle
# Make Operation Handle
## Mark Bend Length
## Clamp Metal Tube
## Torch Bend Region
## Bend Metal Tube

# Make Raisers
## Mark Metal Flat
Get the 1” x 4” x 11” steel flat.
Mark the flat for 2 raisers as shown below:

## Angle-cut the Metal Flat
Use a speed square to orient the metal flat at 45 degrees on the ironworker.
Remove the speed square.
Clamp the metal flat.
Shear the metal flat!

Reclamp one metal flat for the right cut angles.
Shear the first!
Reclamp and shear the second!

## Surface Grind Top and Bottom
15/1000” for top
2/1000” for bottom

# Make Blade Guard
## Drill Thin Metal Flat
## Bend Thin Metal Flat
## Mount Metal Sheet
## Torch Inner Circle
## Torch Outer Circle
## Torch In Half
## Mount Halves
## Weld Thin Metal Flat
# Make Base