Welcome to the Cold Saw Replication Guide.

Refer to the document named Build Preparation for what tools and materials you will need for making the Cold Saw.

During the Build Preparation, identify and organize the items for ease of access during the replication process.

# Cut Materials

## 2” x 3” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
4 – 26mm (1.0236”) for Short Spacers
1 – 50.8mm (2”) for Handle Block
4 – 76.2mm (3”) for Long Spacers
4 – 101.6mm (4”) for Clamp Blocks
4 – 127mm (5”) for Clamp Jaws
2 – 300mm (11.81”) for Swivel Blocks
2 – 400m (15.75”) for Vise Moving Blocks and Vise Fixed Block

## 1” x 4” Steel Flat Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
1 – 140mm (5.513”) for Short Support Flat
1 – 200mm (7.87”) for Bridge Flat
2 – 280mm (11”) for Long Support Flat and Rotation Support Flat

## 1/8” x 1” Steel Flat Lengths
Cut Length Tolerance – 13mm (1/2”)
Cut Angle Tolerance – <5 degree
1 – 101.6mm (4”) for Indicator Flat
2 – 381mm (15”) for Blade Guard Supports

## 3” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
3 – 25.4mm (1”) for Axial-Radial Shaft Collars

## 2” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
6 – 20mm (0.787”) for Shaft Collars
1 – 76.2mm (3”) for Shaft Coupling

## 1.25” Dia Steel Round Lengths
Cut Length Tolerance – 1.6mm (1/16”)
Cut Angle Tolerance – <1 degree
4 – 350mm (13.78”) for Vise Shafts, Handle Shaft, Support Shaft
1 – 700mm (27.56”) for Operation Handle

# Make Blade Guard
## Mount Metal Sheet
## Torch Inner Circle
## Torch Outer Circle
## Torch In Half
## Mount Halves
## Weld Metal Flat
# Make Base